## Slide 1
Introduction to Delft-FEWS

## Slide 2: Deltares & (flood) forecasting
Detection
Warning
Response
Forecasting
Simulation
Deltares
Floods, droughts & operational management
Water quality (incl. spills) and ecology (e.g. algae blooms)
Peat fire
Levee strength
Groundwater modelling
 lead time
Notes: Delft-FEWS has been developed as a flood forecasting system, but in the mean time it is being used for several purposes

## Slide 3: Forecasting… discharge at Lobith (Rhine)
Detection
Warning
Response
Forecasting
Simulation
Monitoring - precipitation
- waterlevels
  water to river: Precipitation + rainfall-runoff model(s) + snow melt
  water in river: Hydrodynamic model (river itself + tributaries)
data acquisition
data validation (errors/gaps)
  collect ‘model’ data
  run model(s)
  running scenarios (manipulating input)
  warning &
  dissemination
  comparing output runs (graphs/tables)
  approving ‘a’ forecast
   quality stamp
Notes: Delft-FEWS has been developed as a flood forecasting system, but in the mean time it is being used for several purposes

## Slide 4: Forecasting…
Aspects
  many individual steps/operations
  use different tools/techniques/software (telemetry, meteo, models)
  time-consuming
  availability of an ‘operator’
Results
  (early) information and data about natural behaviour / events
  action(s): warning/evacuation
To enable all this: Delft-FEWS

## Slide 5: Not only forecasting…
Delft-FEWS also suitable as a:
Platform for (long term) storage of Water Information (WIS)
  Waterboards systems
Platform for Optimization and Real Time Control
  ISA HW (WSHD, NL)
  BPA (Portland, USA)
  Tam Tam (Almere)
Platform for running (long term) models/scenarios
  Deltamodel
Platform for Automatic Data Conversion
  DCM module

## Slide 6: The Delft-FEWS Platform

## Slide 7: Delft-FEWS as platform for operational systems

## Slide 8: Delft-FEWS (international)
Clients
  Environment Agency (UK)
  SEPA (Scotland)
  NWS (USA)
  BfG (D)
  (regional) governments/agencies in Austria, Italy, Spain, Swiss, Taiwan, Singapore, Vietnam/Thailand, Australia etc.
In collaboration with:
  Consultants (Royal Haskoning, JBA, Halcrow, etc.)

## Slide 9: Community Hydrologic Prediction System (CHPS)
National River Forecasting System for…
National Oceanic & Atmospheric Administration (NOAA)
National Weather Service (NWS / OHD)
13 River Forecast Centers (RFC)
  Currently: 7 RFC operational using FEWS
Notes: Karel Heynert
Simone van Schijndel
Peter Gijsbers

## Slide 10: National Groundwater Modelling System for UK

## Slide 11: Delft-FEWS (NL)
Clients
  Municipalities
  Waterboards
  Ministry of PW & Watermanagement (Waterdienst)
In collaboration with:
  NL Consultants (HKV, Nelen & Schuurmans, Hydrologic, DHV, …)
  IBM (Flood Control 2015)
  …

## Slide 12: Delft-FEWS (NL)
WIS Roer en Overmaas
WIS Velt & Vecht
WIS Peel en Maasvallei
AIM Veluwe
FEWS-Rivieren, FEWS-Meren,
FEWS Algen, FEWS Waterbeheer
FEWS IWP
Rijkswaterstaat
BOS Regge & Dinkel
FEWS-LIZARD
Hollands Noorderkwartier
FEWS-LIZARD Waternet
WIS Aa en Maas
FEWS-LIZARD
Hollandse Delta
FEWS-LIZARD
Zeeuwse Eilanden
WIS & BOS De Dommel
BOS Noorderzijlvest
BOS Hunze & Aa’s
WIS HDSR
WIS Vallei en Eem
WIS Zuiderzeeland

## Slide 13: Delft-FEWS (NL) - Waterdienst applications
FEWS North Sea (Water levels/Waves)
FEWS-Rivers (floods Rhine/Meuse)
FEWS-W’Mgmnt (water distribution)
FEWS-RMM (Delta-area, incl SSB)
FEWS-Channels (Gauge Mgmnt)
FEWS-Lakes (Water levels Lake IJssel)

## Slide 14: Delft-FEWS User Community
in development
operational, status unknown
operational service
USA (NWS)
Canada
UK
Netherlands
Germany
Suisse
Italy
Austria
Spain
Singapore
Taiwan
Mekong River Commission
Australia
Sudan
Georgia
Azerbaijan
Zambezi

## Slide 15: Relation with Delft-FEWS User Community…
Longterm relation & commitment
Looking for the added value (science based development & consultancy)
Delft FEWS Policy…
Focus on implementation & development of forecasting sytems → taking responsibility in this process!
Software is carrier of knowlegde (free but no freeware) → high quality software required
Guarantee longterm support commitment
Financing further science & software development by user community (ad-hoc alliances initiated by Deltares) & own R&D
Notes: Longterm relation & commitment with clients (support contracts)

## Slide 16
Delft-FEWS
Open Shell Forecasting System

## Slide 17: Delft-FEWS Philosophy
Generic information platform for data processing for flood and environmental forecasting systems
Links to all kinds of meteorological and observed data sources, such as
  ground station monitoring devices, weather radar,
  numerical weather models and
  satellite images
Facilities to process such data in required formats
Links to a wide range of hydrological and hydraulic modelling systems
Easy to connect models and data sources, irrespective of their producers in order to avoid capital destruction of earlier investments by clients
Resilient system

## Slide 18
Toolbox for development of forecasting systems
Rapid implementation, scalable & flexible
Automatic / manual & stand alone
Fully ‘configurable’ by user
Binding dataflows + models
Real-Time
Delft-FEWS Philosophy

## Slide 19: Delft-FEWS (concept)
Delft-FEWS
import
validation
transformation / interpolation
data hierarchy
general adapter
export / report
administration (data, forecasts)
viewing (data, forecasts)
archiving
…
data (feeds)
models
export &
dessimination
PI / NetCDF
import

## Slide 20: Delft-FEWS Data (import formats)
Grid formats
ArcInfoAscii
BIL
BUFR
COSMO7_COR
DWD-LM
DWD-LM2
DWD-GME
GHD
GRIB
GRIB2
GRIBBASIC
GRIBCOSMO
hdfSoilMoisture
KNMI-HDF5
Landsat-HDF5
MATROOS NetCDF
NetCDF
Nimrod
NimrodMultipleDir
SwissRadar
GrayscaleImage
Scalar
AHD
ArcWat DBF
BC2000
BFG
CSV
DINO
DiverMon
EA
EKSW
EKSW2005
EVN
Era15
FOC
FewsDatabase
hdf4
Hims
Hydris
HYMOSASCII
HYMOS
KNMI
KNMICSV
KNMIEPS
KNMIIRIS
KNMISYNOPS
Mosaic
Scalar (continued)
Msw
Mosm
NOOS
NTURAIN Import
NTUQUARTER Import
PI
PMDSynoptic
PMDTelemetric
RijnlandRTD
SSE
SHD
SHEF
SMA
SMAecmwf
Synop
Tmx
TmxCSV
TTRR
LUBW
WapdaTelemetric
Wiski
WSCCCsv
Wsd
DSS
  https://publicwiki.deltares.nl/display/FEWSDOC/Available+data+types

## Slide 21: Delft-FEWS (concept)
Delft-FEWS
import
validation
transformation / interpolation
data hierarchy
general adapter
export / report
administration (data, forecasts)
viewing (data, forecasts)
archiving
…
data (feeds)
models
export &
dessimination
PI
import

## Slide 22: Exchange of data: published interface
Delft-FEWS
General Adapter
Model Adapter
Model
model
input data
model
output data
published interface
input data
(pi xml)
output data
(pi xml)

## Slide 23: Delft-FEWS External Models – Model Adapters
  CEH Adapters (SNOWP, SNOW, PDM, KW, ARMA, TCM, HEC, GRID2GRID)
  HR (ISIS)
  PlanB Adapters (TRITON & PRTF)
  DHI Adapters (Mike11, NAM)
  Midlands Region (DODO, MCRM)
  Southern Region (STF)
  Northwest Region (NW TF – Common Adapter)
  Wales (SW Overtopping module - Common Adapter)
  SouthWest (Bruton/Holbeam Dam module – Common Adapter)
  Deltares (RTC Tools, Delft3D, SOBEK, RIBASIM, HYMOS, Sacrament, SSARR)
  SMHI (HBV)
  University of Karlsruhe (PRMS)
  JRC (Lisflood - PCRaster)
  NWS (SNOW17, SAC-SMA, UNIT-HG, LAG/K, SARRROUTE, SSARRESV, RESSNGL, BASEFLOW, CHANLOSS, APICONT, CONSUSE, GLACIER, LAYCOEF, MUSKROUT, RSNELEV, SACSMA-HT, TATUM)
  USACE (HEC-RAS, HEC-ResSim)
  http://public.wldelft.nl/display/FEWSDOC/Models+linked+to+Delft-Fews

## Slide 24
Service Oriented Architecture
  operating (business) aspects
  system / platform ‘independent’
Java, XML & JMS
Oracle, PostgreSQL, MS SQLServer
Open Systems Approach…
Can be extended using plug-ins (Modules, Displays)
Transparent configuration using XML file format
External modules can be integrated using XML as exchange format
Provides access to time-dependent data via JDBC, WebServices
Delft-FEWS Software

## Slide 25: Delft-FEWS settings
Stand alone
  all activities are done on (your) local machine (desktop/laptop)
Client-Server
  clients log on to ‘central backend’
    calculations are done on designated machines/servers
    data ‘downloaded’ to local machine (laptop/desktop)
    activities scheduled with fixed intervals (import, forecasts)
    manually invoked activities from clients  queue

## Slide 26: Delft-FEWS system overview (stand-alone)
stand alone

## Slide 27: Delft-FEWS System overview (client-server)
central database
master controller
admin interface
server
client
forecasting shell(s)
FSS
operator client(s)
OC
MC
CDB
AI
configuration
manager
CM
Notes: Client-Server
  clients log on to ‘central backend’
    calculations are done on designated machines/servers
    data ‘downloaded’ to local machine (laptop/desktop)
    activities scheduled with fixed intervals (import, forecasts)
    manually invoked activities from clients  queue

## Slide 28: Delft-FEWS System overview (client-server)
storage of all data
task dispatcher
user management
executing workflows
user
system
management +
scheduling tasks
server
client
= synchronisation
FSS
OC
MC
CDB
AI
configuration
management
CM
Notes: Client-Server
  clients log on to ‘central backend’
    calculations are done on designated machines/servers
    data ‘downloaded’ to local machine (laptop/desktop)
    activities scheduled with fixed intervals (import, forecasts)
    manually invoked activities from clients  queue

## Slide 29: Demonstration
Operator Client: FEWS Noordzee – live/current data

## Slide 30
Delft-FEWS GUI
dropdown menus
button bar
log viewer
map display
status bar
Filters
Locations
Parameters
Open forecasts