## Slide 1
FEWS Static Configuration

## Slide 2: FEWS Static Configuration Data
Location data
  Locations
  Location Sets
  Location Icons
Parameters
  Parameters
  Time Series Display Configuration
  Parameter Unit Conversions
Maps and FewsExplorer
  OpenMap properties
  Grid Display
  FEWS Explorer
Other Static Configurations
  Grids
  Branches

## Slide 3: Locations
Information for each location in the FEWS Config

## Slide 4: Location Icons
Location Icons are used to help identify types of locations
  catchment site
  coastal
  fluvial site
  meteo site
  radar site
Notes: Also a good example of why locationsets are useful

## Slide 5: Grids are locations to FEWS
Grid time series are two dimensional time series
A grid location is required in the locations XML file
The Grids configuration file includes mete-information of a grid
The spatial display can show gridded timeseries

## Slide 6: LocationSets
LocationSets define groups of locations
LocationSets can be nested!

## Slide 7: LocationSets - the meta data approach
XML was the basis for FEWS for many years ...but
Location meta data often managed in other systems (e.g. GIS)
Location coordinates in shape (.shp), associated attributes in tabular form (.dbf)
Introduced to FEWS in 2007/2008
Since 2013 also in .csv files
easier to maintain locations
Location attributes can be used to:
  compose location sets with similar characteristics
  define idmaps (translation tables for importing/export data)
  define threshold crossing values
  define range values for validation rules
  define coefficients for calculations
Notes: 7

## Slide 8: Xml and CSV – the meta data approach
3 step definition
The CSV file defines per location (row) the value for a specific attribute (by column)
LocationSets.xml file tells FEWS how to read the CSV file by allocating ‘%column_name%’ to location attribute
Other configuration files apply these attribute values for various purposes Replace ‘@attribute-name@’ with attribute value
Values example from: NSW_sensors.csv
Notes: 8

## Slide 9: Composing locationSets with location attributes
LocationSets can be generated from another locationSet by using attributes and conditions:
  attribute equals
  attribute contains
  attribute starts with
  id contains
  attribute exists
  …
Notes: Also a good example of why locationsets are useful

## Slide 10: Calculation coefficients via location attributes
Define attributes for Gauge datum correction
Allocate attribute values per sensor
Apply attribute value in calculation
Example from: LocationSets_NSW.xml
Definition is part of locationSet NSW_sensors
Example from: NSW_sensors.csv
Example from: Process_Surge.xml
Notes: 10

## Slide 11: Xml and CSV recap
September 2013
Delft-FEWS Configuration Course
11
XML and CSV 3 step definition
  The CSV file defines per location (row) the value for a specific attribute (by column)
  LocationSets.xml file tells FEWS how to read the CSV file by allocating ‘%column_name%’ to location attribute
  Other configuration files apply these attribute values using ‘@attribute-name@’ for various purposes
 Configuration extension and maintenance shifts to meta data
Notes: 11

## Slide 12: Exercise
Exercise 2: Locations and LocationSets

## Slide 13: Parameters
Parameters are organised into parameter groups with a unique id and name
Parameters have a unique id and a name
The parameter is a primary key in the time series

## Slide 14: Parameters – unit conversions
Units are a property of a parameter group
Units can be converted during importing or exporting activities

## Slide 15: Parameters – time series display configuration
Set default plot attributes per parameter in TimeSeriesDisplayConfig.xml

## Slide 16: Exercise
Exercise 3: Parameter properties
Change some attributes of lines plotted for parameters
  Add minimum and maximum scaling
  Change display precision (default = 3 decimals)
  Change some parameter line colours

## Slide 17: FEWS Maps
FEWS explorer shows map layers & location icons
Map layers:
ArcVIEW, ArcGIS Shape layers
OpenStreetMap, Google earth, Virtual earth
ESRI ASCII grids/images
TIF images
Located in “\MapLayerFiles” or the database
Configuration: “Explorer.xml” (\SystemConfigFiles)
Map layers can be toggled on and off
Scale bar etc. can be switched off via menu

## Slide 18: FEWS Map Layers
Other FEWS component
with map layers:
Spatial Display

## Slide 19: FEWS Maps – Configuration
Geodatum
Projection
Default view extent
Extra extents
Default options
Options to add shapefiles
Options to add grids
Switch to visible

## Slide 20: FEWS Explorer
FEWS Explorer is the main GUI
Includes many configuration elements
Configured through the “Explorer” XML file

## Slide 21: FEWS Explorer – explorer options
Elements that are by default visible
in the status bar when the system is started

## Slide 22: FEWS Explorer – zoom extents
Pre-configured zoom levels that can be selected from FEWS explorer

## Slide 23: FEWS Explorer – tasks
Tasks that can be carried out from the explorer
Text
Icons

## Slide 24: FEWS Explorer – additional settings
Configuration of:
display date time format
time zone
geodatum
cardinal timestep
log panel etc.

## Slide 25: Exercise
Exercise 4: FEWS Explorer Elements
Change explorer visible items on start up
Add predefined zoom level

## Slide 26: FEWS Static Configurations - Profiles
Profile time series are one dimensional time series
A location is required in the locations XML file
Branches configuration file contains the time series

## Slide 27: FEWS Static Configurations - Grids
Grid time series are two dimensional time series
A grid location is required in the locations XML file
Grids configuration file defines the grid
The spatial display file is used to configure the display of grids.