## Slide 1
TimeSeriesSets

## Slide 2: Time Series - What it’s all about
What ?
numbers
When ?
Where ?
Creation
How ?
By Whom ?
When ?
Semantics

## Slide 3: Time Series - What it’s all about
What ?
Parameter
numbers
When ?
Time stamp
Where ?
Location
Creation
How ?
Module instance
By Whom ?
Workflow
When ?
Task run
Semantics
Unit

## Slide 4: Time Series – FEWS concepts
Primary keys for time series identification:
Parameter: Define what the time series represents
Location: Defines where a time series value applies
Time step: Defines when a time series value applies
Time series type: Defines its behaviour in the system
Value type: Defines its internal data format
Module instance: Defines how a time series value is generated

## Slide 5: Time Series – FEWS concepts
Primary keys for time series identification:
Parameter: Define what the time series represents
Location: Defines where a time series value applies
Time step: Defines when a time series value applies
Time series type: External or Simulated, and
Historical (continuous in time) or Forecasting (start time T0)
or Temporary
Value type: Defines its internal data format
Module instance: Defines how a time series value is generated

## Slide 6: Time Series – external historical
10:00
Complete series
Added incrementally
Can be edited by the user
Only new and changed values are stored
Complete series
Manual edit
Time of import
00:00
04:00
07:00

## Slide 7: Time Series – external forecasting
Time of Forecast
Added and stored individually
Can be edited by the user
Usage of series depends on T0
Series at 08:00
Series at 06:00
00:00
04:00
08:00
06:00
00:00
04:00
08:00

## Slide 8: Time Series – simulated historical
System Time
Continuous in time
Referenced by the forecast model that produced them
Approved series shown automatically (including history)
Most often linked by model states
04:00
08:00
12:00
Series at 16:00
Series at 08:00
00:00
04:00
08:00
12:00
16:00
16:00

## Slide 9: Time Series – simulated forecasting
System Time
Continuous in time (in combination with simulated historical)
Referenced by the forecast model that produced them
Approved and selected series can be viewed
Series at 12:00
04:00
08:00
12:00
00:00
04:00
08:00
12:00
16:00

## Slide 10: Time Series – temporary
Referenced by the module instance that produced them
exist ONLY during the run that created the series
  E.g. time series used in pre- / post-processing
module 1
module 2
module 3
temporary series
module 1
module 2
module 3
workflow 1
workflow 2
Notes: 10

## Slide 11: Time Series Sets
Properties of a timeSeriesSet
  Some elements are only used when retrieving time series, other elements only when storing data
All data handling is done through Time Series Sets

## Slide 12: Workflow – FEWS concepts
Module instance - defines processing step
Workflow - Logical sequence of module instances
Task run - Actual execution of a workflow
TimeserieSets connect the dataflow between the module instances
Import
Preprocess
Run Model
Post process
Report
Export
Archive

## Slide 13: General Module layout
anyModule
Request data
from datastore
Do something …
Write data
to datastore

## Slide 14: Time Series Sets - Examples
Import Run General Adapter Run

## Slide 15: Importing data
Import Modules allows data from external sources to be imported
Various Scalars – e.g. PI XML and Wiski
ASCII grid time series
Binary GRIB (grid) and BIL time series
Currently around 50 data import types
FEWS imports files from directories specified in the global.properties file

## Slide 16: Import Module
Key Features:
ID mapping > idMap.xml
Units mapping > unitConversion.xml
Flag mapping > flagConversions.xml
Tolerance: when imported data is not exactly observed at the cardinal time step
Time zone mapping: database stores all data in GMT, specify time zone when importing
  Validate: Imported files can be validated against their own schema

## Slide 17: Import Module & Id mapping
Matching ‘outside world’ to the ‘FEWS world’
  locations (ids)
  parameter (ids)
Three levels
  direct mapping  location names AND parameter names differ
  indirect  either location names or parameter names differ
  1:1  location and parameter names do NOT differ
Used when importing and exporting time series
Notes: Id mapping files are in the id mapping folder and should be “registered” in the appropriate descriptors file.

## Slide 18: Import Module & Unit conversion
Map internal units to external units
Used when importing and exporting time series
Extra option to convert datum of level recordings (external unit mAOD)

## Slide 19: Import Module & Flag conversion
Map internal quality flags to external quality flags
Used when importing and exporting time series

## Slide 20: Exercise
Exercise 5: Import time series
Add elements to ID mapping table
Run import workflow
Analyse data with the Time Series Display

## Slide 21: Validating Data
Allow quality checking of all scalar time series data
Difference in hard limit and soft limit checks
  Hard limit checks mark data as unreliable
  Soft limit checks mark data as doubtful
  Option to enter monthly limits
Specify rule for 1 time series or a complete set

## Slide 22: Exercise
Exercise 6: Add validation rules for imported data
Check the data just imported
Define validation rules
Enter the rules in the ValidationRuleSets XML file
Delete the data store
Run import workflow
View data
Check the difference!