## Slide 1
Delft-FEWS
Basic Configuration Course
(continued)

## Slide 2
Processing data

## Slide 3: Data processing
Data import
Pre-processing (transformations)
Pre-adapter
Run model
Post-adapter
Post-processing
Visualisation
Pre-processing of model input
Post-processing of model output

## Slide 4: TransformationModule
Data processing can be done using the transformationModule in FEWS.
This transformationModule contains a wide range of functionality
relevent to this.
Some examples:
User transformations: simple data manipulation (A+B, etc)
Data interpolation and extrapolation (spatially and temporally)
Aggregation and disaggregation
Statistics
And much more…
http://publicwiki.deltares.nl/display/FEWSDOC/20+Transformation+Module+%28Improved+schema%29

## Slide 5: TransformationModule
Basic structure:
Input and output
variables
Transformations

## Slide 6: Transformation - Configuration
https://publicwiki.deltares.nl/display/FEWSDOC/20+Transformation+Module+%28Improved+schema%29

## Slide 7: Transformation Module – Interpolation
7
Serial Interpolation methods
  Default
  Block
  Linear
  Extrapolation
Spatial Interpolation methods
  Average
  Bilinear
  Closest distance
  Inverse distance
  Kriging
  Max / min
  Sum
  Thiessen polygon
  Triangulation
  Weighted
Notes: 7

## Slide 8: Exercise
Exercise 9: Fill gaps in imported timeseries
Analyse module that fills gaps in the water level time series
Add the new module instance to the module instance descriptors
Configure a workflow that executes the interpolation module instance
Check results!

## Slide 9: Transformation Module - Interpolation
Possible problems / Issues to note
Time Series Set to Interpolate
  ModuleInstanceId of series!!! (ImportTelemetry)
  Relative View Period
When interpolating to fill gaps
  Input time series same as output time series
Using LocationSets and/or Locations
  Linear interpolation – can be done using a locationSet
  Default – take care as default value may vary per location

## Slide 10: Transformation Module - Examples User defined function

## Slide 11: Transformation Module - Examples User defined function
Different function / parameters per segment / range
Define ranges in rating curves file / coefficientsets file

## Slide 12: Transformation Module - Examples User defined function
Generic function parser used
“Any” function can be defined

## Slide 13: Transformation Module - Examples Rating curve
Same approach as other transformations using stageDischarge class
Convention on inputId / ouputId & parameter names
Rating curves are contained in the CoefficientSetFiles (RatingCurves.xml)
Rating curves are linked to locations
One location or locationSet
Use coefficients from CoefficientSetFile

## Slide 14: Transformation Module - Examples Rating curve
CoefficientSets
StageDischargeCoefficientSets.xml (name not fixed)
In CoefficientSetsFiles folder
Referenced in Transformation ModuleInstance
Rating curve defined only once
Referenced by locationId

## Slide 15: Transformation Module - Examples Weighted averaging
Convention on inputId / ouputId & parameter names
formula: (X1 * a + X2 * b + X3 * c) / (a + b + c)
number of locations is flexible, missing locations will be left out

## Slide 16: Transformation Module - Examples Data Hierarchy / Merge
used first
used second
used third
Fallback options to complete a series

## Slide 17: Transformation Module – Example Typical profile
Examples of typical profile use:
  Evaporation series (one value per calendar day)
  Temperature variation across day

## Slide 18: Exercise
Exercise 10: Add rating curves
Add rating curve for location Hydro1
Analyse transformation file
  register module instance in descriptors file
  add module instance to the exercise workflow

## Slide 19: Exercise
Exercise 11: Add catchment averaging rules
Averaging rainfall data from 2 locations into 1
create a new location
adding weights to (input) series to create new output series for this location
register module instance in descriptors file
add module instance to the exercise workflow