## Slide 1
Delft-FEWS
Basic Configuration Course
(continued)
Notes: Live System Aspects
Organising the live system
Components of a live system
Workflows - Running
Workflows – Scheduling
Triggered Workflows (het principe)
(Synchronisation)
Tool – Admin Interface:
Health Checking/Status Information
Workflow Load Balancing (mapping)
Workflow Overview (Scheduled Tasks)
Scheduling
Configuration
Configuration Manager
How Config Files/Patches are being distributed?
Optimizing the Live System
Monitoring
Configuration aspects (expiry time, synchLevel, valueResolution)
Maintenance Workflows
Amalgamate
Database Analysis
Advanced
Multi MC Systems
Duty-standby
Event-action configuration

## Slide 2
Live systems (advanced)

## Slide 3: Table of contents
Tools: Admin Interface
Tools: Configuration manager
Live system and configuration
Maintenance
Advanced topics

## Slide 4: Tools operational system
Configuration Manager
Administrator Interface (AI)
Demonstration
Demonstration

## Slide 5: Delft-FEWS system overview
central database
master controller
forecasting shell(s)
operator client
admin interface
server
client
FSS
OC
MC
LDS
AI
configuration
manager
CM

## Slide 6: Tools – Admin Interface
Administration tool for live system
Direct access to Master Controller
Main tasks
  Monitoring (health) of live system components
  Scheduling of tasks (current!)
  Monitoring of task queues
  Management of Forecasting Shell Servers
  Monitoring Data Feeds
  Setting enhanced forecasting etc.

## Slide 7: Logging in

## Slide 8: System Status
Overview of all central / vital components
Task Queues
MC Status
Forecasting Shell Servers
MC-Components
MC Version
DB Status
JMS Status
Admin Interface Version

## Slide 9: View Logs
Overview of Log messages
Master Controller
(are not displayed in OC)
(Type 0)
Forecasting Shell Server
(are also displayed in OC)
(Type 1)
Additional types:
(also displayed in OC)
Type 5 (created on OC)
Type 8 (special MC messages)

## Slide 10: Collect system log files
Download log files from Mastercontroller, Forecasting Shells and Admin Interface as one zip file
Also provides extra information:
  On disk space, server load, network connectivity (Systemreport.log)
  Scheduled tasks on MC (ScheduledTasks.xml)

## Slide 11: Overview of Import data
Monitor data feeds
Date / time of last import for each directory

## Slide 12: Overview of scheduled processes
- Overview of scheduled processes (“Tasks”)
- Scheduling of new processes
- Current Forecasts

## Slide 13: Overview executed processes
Click on “Task Runs” link of “Scheduled Task”
List of past Task executions (“Task runs”)
Display of status:
  Complete
  Failed
  Terminated

## Slide 14: Overview of Task Queue
FSS-ID indicates, where the process is currently running
Manage processes
  Stop/kill if desired
Processes that have been queued for 10 minutes are not executed, e.g. when no FSS is defined or available.
List of processes (“Task runs”):
  running
  queued

## Slide 15: Scheduling a new task
Similar to Manual Forecast display in OC:
- Select Workflow
- Enter TAG, only for “enhanced” forecasts
- Next due time
- Repeat time (empty for single task run)
- Shift T0
- Approve (to make forecast current)
- Run on failover (not in OC)

## Slide 16: Managing Processes / Workflows
Workflows tab
- Overview of all Workflows in the central database
- Upload of new Workflows (is no longer used)

## Slide 17: Workflow – FSS Mapping
Determines where Workflows are executed
Specific Forecasting Shell Server
  Model dependent (e.g. ISIS)
  FSS Rolling Barrel
One at a time
  Import
MC Processes (mapped automatically)
  *synch

## Slide 18: System Control
Start / Stop Master Controller
BE CAREFUL !
- Setting MC Failed status (only for systems with 2 or more MCs)
- Initiating MC startup or MC shutdown

## Slide 19: Recent Developments: Database Analysis

## Slide 20: Trend Analysis – Admin Interface
How many records have been added to the database
Number of records added to (relevant) tables in the database since 1 Year, x Months, x Weeks, x Days, …
Estimate of memory usage of (relevant) tables in the database since 1 Year, x Months, x Weeks, x Days, …
How many records/bytes will be expired (and ‘rolling barreled’)….
Number of records which will be removed from (relevant) tables of the database within x Days, x Weeks, x Months, 1 Year from now…
Estimate of available memory caused by removal of records from (relevant) tables of the database within x Days, x Weeks, x Months, 1 Year from now…
Option to add a user-defined period.

## Slide 21: Trend Analysis – Admin Interface

## Slide 22: Delft-FEWS Configuration Stand alone vs Operational environment
Configuration
Database
  Stored in different tables
  in operational environment
OR
File System (+ directory structure)
  Stored in different files
  Ordered in subdirectories
  during development/testing

## Slide 23: Tools – FEWS Configuration Manager

## Slide 24: Configuration Manager
A special version of an operator client
Different GUI
Objective: Version Management of Configuration Files
Import (new or updated) individual files, folders or a complete /Config/ directory
Upload to Central Database

## Slide 25: Tools – Configuration Manager
user
OC
local datastore
Management of the configuration files
To the central database
update XML-files
import to OC
set files (in-)active validate changes
upload config change to MC
To the file system
download configuration to OC
export from OC to file system
go to 1
files
5
4
6
2
1
3
central database
e.g. oracle

## Slide 26: Patch Mechanism (OC/FSS)
A patch (e.g. 2014.01_Patch.jar) is a piece of code-fixes which is treated as ‘configuration file’ in the rootConfigFiles directory
Is distributed like all other configuration files
  Import into Config Manager
  Upload to Master Controller/Central Database
  Downloaded in the next run to all FSSs
  Downloaded to every OC which is logging on (ask for restart)

## Slide 27: Optimizing your configuration
Monitoring
Configuration aspects (expiry time, synchLevel, valueResolution)
Maintenance Workflows
Amalgamate

## Slide 28: Monitoring
Using the tools in the Admin Interface we can monitor database usage of a live system
But how can we optimize this (with regard to performance)?

## Slide 29: TimeSeries in a Client-Server system
A FEWS Client Server System uses the same configuration as a Stand
Alone system
  When updating the configuration of a FEWS application, always use the Stand Alone system
  It is good to know how the Client-Server FEWS system works
  The configation has some special features with respect to:
    Synchronisation
    Expiry time
    Precision used to store the data

## Slide 30: Time Series Sets
Properties of time series:
location Id – or – locationSetId
parameter Id
timestep
relativeViewPeriod
valueType (scalar, grid, profile, ..)
timeSeriesType (external historical, external forecast, ..)
moduleInstanceId (import, PDM, KW, ISIS, ..)
readWriteMode
expiryTime (when to delete from database)
synchLevel
simple transformations (delay, multiplier, divider, incrementer)
ensembleId

## Slide 31: Limits of FEWS Databases
Central database – ORACLE, PostGress, SQLServer
  No size limit
Forecasting Shell databases
  Microsoft ACCESS: 2 GB size limit
  Firebird: No size limit
Operator client databases
  Microsoft ACCESS: 2 GB size limit
  Firebird: No size limit
Of course: performance will reduce when database is larger

## Slide 32: Expiry Times
The total volume of data in the database can be reduced by :
  Configuring the expiry time
  Reducing the number of decimals for data values
  Mark time series as temporary data (not synchronised)
The maintenance task RollingBarrel deletes all expired data
  From the Central database (every 30 minutes)
  From the Forecasting Shells (every 24 hours)
  From the Operator Clients (every 30 minutes)

## Slide 33: Configure valueResolution of parameters
By default a value is stored using 8 decimals
Most observed data are imported with only 2-3 decimals
The Parameters XML file allows configuration of valueResolution
This can reduce the size of the data volume considerably

## Slide 34: Database size and synchronisation optimisation
Size of the database is mainly determined by:
  Size of the Simulated Forecast time series or External Forecast time series
  Number of forecast runs a day
  Length of time a forecast is held in the database (expiryTime)
  Observed grids
Size of Simulated Forecast time series can be limited by:
  Change Expiry Time for less important time series or grids
  Not synchronising or storing all time series, only what you want to see on the OC
  Use valueResolution for parameter groups
Size of Observed Gridded Data can be limited by:
  Cut-out the area of interest

## Slide 35: Maintenance Workflows: Rolling Barrel
Each time series in FEWS has an associated expiry time. Once this expiry time is exceeded, this time series will be removed from the database by means of a mechanism called the Rolling Barrel
For the OC (client) the rolling barrel runs at start-up/shutdown, with a pre-set interval, or can be disabled
For the Forecasting Shells and Central Database, the Rolling Barrel should be setup as a scheduled task

## Slide 36: Maintenance Workflows: markedRecordManager
The MarkedRecordManager task has to be run on the Forecating Shells and Central Database to remove database records that have been marked for deletion. The MarkedRecordManager should be setup as a scheduled task.

## Slide 37: Amalgamate
Time series are stored in the FEWS database as blobs (“Binary Large OBSjects”; collection of data stored as a single entity in the database)
Regular data imports can generate a large number of small blobs
Because of this, the number of records in the database can become very large
This can degrade performance of the database
The Amalgamate module in FEWS can combine many smalls blobs into larger smaller number of larger blobs, thus reducing the number of records in the database. This Amalgamate module can be run as a regular scheduled task.

## Slide 38: Advanced Topics
Multi MC Systems
Duty-standby
Event-action configuration

## Slide 39: Multiple MC systems
An operational (forecasting) can exist of more than one MC(+FSSs+CDB)
Duty (MC00) and Standby (MC01). MC01 takes over when MC00 is ‘down’. If MC00 recovers, MC00 is ‘duty’ again.
This can be extended to MC03, MC04. Order which MC takes over is configurable;
The arrows mean ‘MC to MC synchronisation’ (every 5 min, hot standby)
Sometimes a MC-system is only ‘receiving’ (pulling) data e.g. for test or research
MC00
Amsterdam
MC01
Delft
MC03
Rotterdam

## Slide 40: Event – Action Configuration
MC can react on a log message
- Increased frequency of Forecasts (e.g. every 3 instead of every 12 hours.)
- Export data after a new Current Forecast becomes available.